SECTION 10 11 00

VISUAL DISPLAY BOARDS

GENERAL

SECTION INCLUDES

Aluminum Framed Magnetic Dry-Erase Whiteboards

RELATED SECTIONS

Section 09 00 00 - Finishes.

Section 09 70 00 - Wall Finishes.

Section 09 90 00 - Painting and Coating.

REFERENCES

ASTM B221 – Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Shapes, and Tubes.

ANSI Z97.1 Safety Glazing Materials Used in Buildings - Safety Performance Specifications and Methods of Test

SUBMITTALS

Submit under provisions of Section 01 30 00 - Administrative Requirements.

Product Data: Manufacturer's data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

Shop Drawings: Provide for each type of visual display board including section details indicating trim, face material, colors, core and backing materials, dimensions, joint locations and special anchor details.

Verification Samples: Submit samples not less than 12 inch square and framed on two adjacent sides, to illustrate materials, finish, color, and configuration of each type of visual display board required.

Manufacturer's Certificates: Certify products meet or exceed specified requirements.

Closeout Submittals: Provide manufacturer's maintenance instructions that include recommendations for cleaning, stain removal and maintenance of all components.

QUALITY ASSURANCE

Manufacturer Qualifications: Minimum 5 years documented experience manufacturing similar products.

Installer Qualifications: Minimum 2 years documented experience installing similar products.

Mock-Up: Provide a mock-up for evaluation of surface preparation techniques and application workmanship.

Finish areas designated by Architect.

Do not proceed with remaining work until workmanship, color, and sheen are approved by Architect.

Refinish mock-up area as required to produce acceptable work.

Accepted mock-ups shall be comparison standard for remaining Work

DELIVERY, STORAGE, AND HANDLING

Deliver and store products in manufacturer's unopened packaging bearing the brand name and manufacturer's identification until ready for installation.

Handle materials to avoid damage.

PROJECT CONDITIONS

Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results. Do not install products under environmental conditions outside manufacturer's absolute limits.

PRODUCTS

MANUFACTURERS

Acceptable Manufacturer: Magnatag Visible Systems, which is located at: 2031 O'Neill Rd.; Macedon, NY 14502-8981; Toll Free Tel: 800-624-4154; Tel: 315-986-3033; Fax: 315-986-4000; Email: request info (info@magnatag.com); Web:www.magnatag.com

Substitutions: Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01 60 00 - Product Requirements.

SPECIAL DISPLAYS

Aluminum Framed Magnetic Whiteboards

Materials

Writing Surface and Edges: Tension-leveled, 22 gauge (0.0299 inches or 0.72 mm) magnetic steel with MagnaLux proprietary white dry-erase finish; fabricated and formed into frameless, self-edged, magnetic whiteboard with fully rounded corners.

Honeycomb core material is made of commercial grade honeycomb Kraft paper consisting of 80 percent recycled material.

Core: 1/2 inch (25 mm) cellular fiber.

Weight: 1.35 lb./ft.2.

Back: Textured aluminum sheet is 24 gauge (0.0239 inches) (0.607 mm).

Aluminum alloy backer conforms to ASTM standard B209, H3105-H234.

Panel Type: As specified

Fire Resistance: Class A; Flame Spread 5 or less, Smoke Developed 25 or less; in accordance with ASTM E 84.

Sizes:

18 inches High by 2 feet Wide

2 feet High by 18 inches Wide

2 feet High by 3 feet Wide

2 feet High by 4 feet Wide

3 feet High by 2 feet Wide

3 feet High by 3 feet Wide

3 feet High by 4 feet Wide

3 feet High by 5 feet Wide

4 feet High by 2 feet Wide

4 feet High by 3 feet Wide

4 feet High by 4 feet Wide

4 feet High by 5 feet Wide

4 feet High by 6 feet Wide

4 feet High by 8 feet Wide

4 feet High by 9 feet Wide

4 feet High by 10 feet Wide

4 feet High by 12 feet Wide

EXAMINATION

Verify that substrates are properly prepared to receive visual display boards.

Do not begin installation until substrates have been properly prepared.

If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

PREPARATION

Clean surfaces thoroughly prior to installation.

Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

INSTALLATION

Install in accordance with manufacturer's instructions.

Install visual display boards level and plumb, keeping perimeter trim aligned in accordance with manufacturer's recommendations.

ADJUSTING AND CLEANING

Verify that all accessories are installed as required for each unit.

Upon completion of installation, clean surfaces and trim in accordance with manufacturer's recommendations, leaving all materials ready for use.

PROTECTION

Keep materials in manufacturer’s original packaging until installation.

Protect installed products until completion of project.

Touch-up, repair or replace damaged products before Substantial Completion.

SCHEDULES

:

:

END OF SECTION